## Slide 1: BE-500XC Series
Elite Version

## Slide 2
1/4” Sharp CCD and Sharp DSP
Auto White Balance
Back Light Compensation
2 Models
  Horizontal (Mirror/Normal)
  Vertical (Mirror/Normal)
Single Bolt mount
154° Viewing Angle
BE 500XC Series Features
Notes: No Microphone
No IR LED

## Slide 3
1 x BE-500XC C – Camera Only
1 x BE-500XC CA – Cable Adapter
1 x BE-500XC Fix – Fixing Pack (6 parts)
1 x BE-500XC IG – Installation Guide
BE 500XC Components

## Slide 4
Horizontal Flush Mount
  BE-500HC
Vertical Flush Mount
  BE-500VC
BE 500XC Installation

## Slide 5
BE 500XC Connection

## Slide 6
Operating Voltage: 12 Vdc
Imaging Devices: CCD - ¼” Sharp/DSP – Sharp
TV System: PAL
Picture Elements: 512 (H) x 582 (V)
Visual Resolution: 380 TV Lines
Required Illumination: 0.1 Lux
Viewing Angle: 122° (H), 94° (V), 154° (D)
Camera Housing: IP68
Operating Temperature: -25° to +80°C
Storage Temperature: -40° to +90°C
Vibration Rating: 10 G
BE 500XC Specification

## Slide 7
Recreational Vehicles
Waste Management
Warehousing & Distribution
Passenger Carrying
BE 500XC Application